## Slide 1: Hazard, Exposure, Vulnerability
Lecture Dr. James Doss-Gollin

## Slide 2: What Is a Fair Insurance Premium?
You own a house in a flood zone.
An insurance company offers you a policy.
How do they decide what to charge you?
Today: The math behind flood risk pricing.
Notes: Target: 1:00. Open with a question that motivates the math.

## Slide 3: Quick Estimate
A house faces two possible flood scenarios this year:
Scenario | Probability | Damage
No flood | 80% | $0
3 ft flood | 20% | $50,000
Notes: Target: 1:03. Get brains working immediately. Give 30 seconds to think, then cold call 2-3 students.

## Slide 4
What’s the expected annual damage?
(30 seconds to think)

## Slide 5: Quick Estimate: Answer
This simple calculation is the core of risk analysis.
Today: How do we do this when floods and damages are continuous?
Notes: Target: 1:05. Key insight: we weight by probability.

## Slide 6: Today
Define key vocabulary: hazard, exposure, vulnerability
See how these combine to produce risk
Learn why (Jensen’s inequality)
Introduce Monte Carlo for complex damage functions
Notes: Target: 1:07. Quick roadmap.

## Slide 7: Risk Analysis Vocabulary

## Slide 8: Hazard
Hazard: The physical event or phenomenon
Flood depth at a location
Wind speed during a storm
Ground shaking from an earthquake
Extreme temperature
Key insight: Hazards are characterized by probability distributions, not single values.
Notes: Target: 1:10. Emphasize that hazard is the physical event, not the damage.

## Slide 9: Exposure: What’s at Risk?
Notes: Target: 1:12. Exposure is about WHAT is at risk, not how vulnerable it is.

## Slide 10
Exposure = assets that could be affected
Buildings and infrastructure
People and livelihoods
Agricultural land
Economic activity
Figure 1: Global flood exposure has grown 10× since 1970. Source: (jongman_exposure:2012?)

## Slide 11: Exposure Changes Over Time
Figure 2: Houston’s built footprint 1800-2018. Development into flood-prone areas increases exposure. Source: (tedesco_exposure:2020?)
Notes: Target: 1:14. Local example: Houston’s footprint has exploded.

## Slide 12: Vulnerability
Vulnerability: Propensity to suffer damage given exposure to hazard
Important distinction:
Fragility: Probability of failure (binary)
Vulnerability: Degree of damage (continuous, 0-1)
Notes: Target: 1:16. This is where depth-damage functions come in.

## Slide 13: Fragility vs. Vulnerability
Figure 3: Fragility surfaces (a) and curves (b) show probability of damage given hazard intensity. Source: Gidaris et al. (2017)
Notes: Target: 1:18. Show the Gidaris figure - panel (a) is a 3D fragility surface, panel (b) shows fragility curves.

## Slide 14: Depth-Damage Functions
For floods, depth-damage functions quantify vulnerability:
Figure 4: Empirical depth-damage from NFIP claims data. Boxplots: Wing et al. (2020) analysis. Lines: USACE engineering curves.
Notes: Target: 1:20. Show the Wing figure. Discuss the huge uncertainty in these relationships.

## Slide 15: What Do You Notice?
From the depth-damage data:
Damage increases with depth (obvious)
Huge uncertainty at any given depth
Empirical data differs from engineering curves
First foot of water causes significant damage
Notes: Target: 1:22. Pause and ask students what they observe.

## Slide 16: From Components to Risk

## Slide 17: Risk = f(Hazard, Exposure, Vulnerability)
The fundamental equation:
where is the hazard intensity (e.g., flood depth).
For expected damages, we integrate over the hazard distribution:
Notes: Target: 1:24. Core equation for the course. Write on board.

## Slide 18: Annual Expected Damages at Scale
Figure 5: From hazard and exposure data through damage models to expected annual damage (EAD). Source: de Moel, van Vliet, and Aerts (2014)
Notes: Target: 1:26. This figure shows the full workflow from data to expected annual damage.

## Slide 19: Your Turn
A city is deciding whether to build a new seawall.
Identify the hazard, exposure, and vulnerability.
Discuss with a neighbor for 60 seconds.
Notes: Target: 1:28. Give students 60 seconds to think. Then cold call 2-3 students.

## Slide 20: Convolution: Hazard → Damages

## Slide 21: The Key Mathematical Idea
We have:
A hazard distribution : probability of each flood depth
A damage function : damage given flood depth
We want:
The damage distribution : probability of each damage level
This transformation is called convolution.
Notes: Target: 1:32. This is the bridge to Friday’s lab. Draw on board if helpful.

## Slide 22: Convolution Illustrated
Notes: Target: 1:34. Simple example to build intuition.

## Slide 23
Hazard Distribution
50% chance: no flood (h=0)
30% chance: minor flood (h=2ft)
20% chance: major flood (h=6ft)
Damage Function
h=0 → $0 damage
h=2ft → $10,000 damage
h=6ft → $100,000 damage

## Slide 24
Damage Distribution:
50% chance: $0
30% chance: $10,000
20% chance: $100,000
Expected damage = $0.5(0) + 0.3(10k) + 0.2(100k) = $23,000

## Slide 25: Jensen’s Inequality
For any nonlinear function :
This will be on assessments. Know it.
Notes: Target: 1:36. Critical conceptual point. This equation WILL be on assessments. Draw convex function with secant line above curve.

## Slide 26: Jensen’s Inequality: Example
Notes: Target: 1:38. Concrete example demonstrating the inequality.

## Slide 27
Hazard:
50% chance: 2 ft flood
50% chance: 8 ft flood
ft
Damage function:

## Slide 28
The difference matters: $27,500 underestimate.

## Slide 29: Why Monte Carlo?
For continuous distributions, expected damage is an integral:
This integral is intractable for nontrivial damage functions or probability density functions.
Solution: Monte Carlo integration approximates it with samples.
Notes: Target: 1:40. Connect Monte Carlo to the integration problem.

## Slide 30: The Law of Large Numbers
If we draw samples from :
The sample average converges to the true expected value.
More samples → better approximation
Notes: Target: 1:42. Keep it simple - just the intuition.

## Slide 31: Monte Carlo Recipe
Sample flood scenarios from hazard distribution
Apply damage function: compute for each
Summarize the damage samples
Once we have samples, we can compute any statistic:
Mean (expected annual damage)
Variance (how much does damage vary year-to-year?)
Quantiles (what’s the 99th percentile damage?)
This is exactly what you’ll implement on Friday.
Notes: Target: 1:43. Procedural summary connecting to lab.

## Slide 32: Extreme Value Theory

## Slide 33: Why Extremes Matter
Most flood damage comes from rare, extreme events.
The problem: Normal distributions underestimate extreme risks.
We need specialized tools for modeling the tails of distributions.
Notes: Target: 1:44. Just planting the seed here. Deeper coverage in Week 4.

## Slide 34: The GEV Distribution
The Generalized Extreme Value (GEV) distribution is designed for annual maxima.
Three parameters:
(location): Where the distribution is centered
(scale): How spread out it is
(shape): How heavy the tail is
means fat tails: extreme events are more likely than a normal distribution predicts.
Notes: Target: 1:45. Keep it light. Just enough to use in lab.

## Slide 35: GEV in Practice
In lab on Friday, you will:
Define a GEV distribution for storm surge
Sample thousands of possible flood scenarios
Pass each through a depth-damage function
Analyze the resulting damage distribution
This is uncertainty quantification in action.
Notes: Target: 1:46. Preview what they’ll do in lab.

## Slide 36: The House Elevation Problem

## Slide 37: A Concrete Decision
Notes: Target: 1:47. Set up the problem students will use all semester.

## Slide 38
A homeowner faces a choice:
How high should I elevate my house?
Higher elevation = more upfront cost, but less future flood damage.
House elevation in Meyerland, Houston. Photo: Allison Lee / Houston Public Media

## Slide 39: The Trade-off
Elevate 0 feet: No construction cost, high expected damages
Elevate 14 feet: High construction cost, near-zero damages
Somewhere in between: ???
Finding the optimal elevation requires:
A hazard model (GEV distribution for surge)
A damage model (depth-damage function)
A cost model (construction costs by elevation)
Notes: Target: 1:48. Draw on board if helpful.

## Slide 40: This Semester’s Sandbox
We’ll use the house elevation problem throughout the course:
Week | Topic | What We Add
2 | Hazard-Damage Convolution | Basic Monte Carlo
3-5 | Risk Metrics | EAD, VaR, CVaR
6-8 | Decision Analysis | Optimal static decisions
10-13 | Deep Uncertainty | Robust optimization
Notes: Target: 1:48. Connect to the iCOW model and SimOptDecisions.

## Slide 41: Wrap Up

## Slide 42: Key Takeaways
Risk emerges from the interaction of hazard, exposure, and vulnerability
Exposure is growing: More assets in harm’s way
Convolution transforms hazard distributions into damage distributions
Monte Carlo lets us handle complex, nonlinear systems
The house elevation problem gives us a concrete sandbox
Notes: Target: 1:49. Summarize main points.

## Slide 43: Lab Preview: Friday
On Friday, you will:
Define a GEV distribution for storm surge
Implement a depth-damage function
Use Monte Carlo to compute damage distributions
Extend to 100 houses at varying elevations
Begin using the SimOptDecisions.jl framework
Notes: Target: 1:50. Connect to Friday’s lab.

## Slide 44: References
Gidaris, Ioannis, Jamie E. Padgett, Andre R. Barbosa, Suren Chen, Daniel Cox, Bret Webb, and Amy Cerato. 2017. “Multiple-Hazard Fragility and Restoration Models of Highway Bridges for Regional Risk and Resilience Assessment in the United States: State-of-the-Art Review.” Journal of Structural Engineering 143 (3): 04016188. https://doi.org/10.1061/(ASCE)ST.1943-541X.0001672.
Moel, Hans de, Mathijs van Vliet, and Jeroen C. J. H. Aerts. 2014. “Evaluating the Effect of Flood Damage-Reducing Measures: A Case Study of the Unembanked Area of Rotterdam, the Netherlands.” Regional Environmental Change 14 (3): 895–908. https://doi.org/10.1007/s10113-013-0420-z.
Wing, Oliver E. J., Nicholas Pinter, Paul D. Bates, and Carolyn Kousky. 2020. “New Insights into US Flood Vulnerability Revealed from Flood Insurance Big Data.” Nature Communications 11 (1, 1): 1444. https://doi.org/10.1038/s41467-020-15264-2.